## Slide 1: Kudzu Leaf (Pueraria montana) Peroxidase Activity
Dr. Raner and Kathryn Briley

## Slide 2: Peroxidase Enzymes
Industrial and biotechnological applications
  Ease of purification
  Broad range of chemical activities
  Low cost for use
Potential problem: poor selectivity

## Slide 3: Diagnostic Abilities
Note. AG represents antigen, AB 1 the antibody from the patient’s blood, and AB 2 the secondary antibody bound to a substrate.

## Slide 5: Common Enzyme Sources
Enzymes produced by a large percent of plant and fungal organisms
  Varying levels of activity
  Horseradish

## Slide 6: Research Goals
Broad goal- explore peroxidase activities from a large sampling of plants
Specific goal - to determine the enzyme stability, optimal pH conditions, and possible novel chemical activities for kudzu

## Slide 7: Kudzu: Pueraria montana
Invasive species
High catalytic activity
Notes: Tube has crude sample or 40-70% precipitate

## Slide 8: Guaiacol Reaction

## Slide 9: Guaiacol Analysis
Notes: reaction mixture composed of 4 mM guaiacol, 4 mM hydrogen peroxide, 50 mM phosphate buffer pH 7.5, and deionized water

## Slide 10: Purification
Extraction
Centrifuge
.
Saturation
.
.
Dialysis
Column Chromatography
Notes:   Extraction
  Centrifuge
  Saturation with Ammonium Sulfate
  Column Chromatography
    (abnormal)
    Saturated solution was passed through a DEAE Sephacel column
  Dialysis

## Slide 11: Pursuit of Optimal pH
Notes: Same rxn mixture

## Slide 12: Peroxidase Quantification via Heme Analysis
Chart: Heme Standard Curve
| 16.8 | 8.4 | 4.2 | 2.1 | 1.05 | 0.525
Area | 728.0358 | 335.8886 | 175.1565 | 74.2863 | 32.3582 | 12.6232
If a value for y is discovered, then the x (heme concentration) value can be calculated
Notes: METHOD:
Concentration measured by absorbance in the spectrometer and using the known extinction coefficient for HRP
1:1 dilution
M1V1=M2V2, with M and V representing molarity and volume
HPLC was used to measure the amount of heme activity in the samples (rxn mixture of 50% acetonitrile, 50% deionized water, and 0.1% trifluoroacetic acid)

## Slide 13: Kudzu Heme Analysis
Integration Value = 4
Heme peak
(the y value)
y = 43.82x - 15.167
Heme concentration = 0.44 mM
Notes: Same rxn mixture

## Slide 14: Purification Assessment
A
B
C
Lane A- Purified Peroxidase
Lane B- Crude Kudzu
Lane C – Protein Ladder
Peroxidase protein size: approximately 30,000 or significantly below

## Slide 15: Future Research
Efficient purification method
Determining specificity for industrial use
  Optimal pH
  Guaiacol screening with varying temperatures
  Determination of variance from unique harvest locations